## Slide 1
Stretchable
OLED Pixel Circuit
Hoseo Univ.
ED LAB.
Master 1st Course
Park Seong Min
2017. 01. 13

## Slide 2
Proposed Pixel Circuit
Ⅰ
Simulation
Ⅱ
Conclusion
Ⅲ
CONTENTS

## Slide 3
Circuit & Timing Scheme
1
Writing Period
2
Compensation Period
3
Proposed Pixel Circuit
Ⅰ
Emission Period
4

## Slide 4
Proposed Pixel Circuit
VDD
SCAN(n)
DATA
GND
M2
M1
Cst
Cs
M4
M3
Node P
SCAN(n)
SCAN(n+1)
DATA
Node P
Figure 2. Timing Scheme
GND
SCAN(n+1)
Figure 1. Proposed Pixel Circuit Schematic
1
2
3
OLED
Stretching
Rigid
Notes: 제안된 회로도와

## Slide 5
Circuit Timing Scheme
SCAN(n)
SCAN(n+1)
DATA
Node P
Writing period
1
2
3
IOLED
VDD
SCAN(n)
DATA
GND
M2
M1
Cst
Cs
M4
M3
Node P
GND
SCAN(n+1)
OLED
When Scan(n) is applied, the voltage of Node P becomes the DATA voltage through M1.
The current flows to the OLED through the VDD, and the OLED emits light. However, since the OLED is short in time compared to the frame time, it is ignorable.
Due to the coupling effect between CST and CS, the DATA voltage of the node P is maintained during this period.
Figure 1. Proposed Pixel Circuit Schematic
Figure 2. Timing Scheme
Notes: Scan(n)이 인가되면서 M1을 통해 Node P의 전압이 DATA 전압이 된다.
VDD를 통해 OLED에 전류가 흐르게 되어 발광하게 되지만 프레임 시간에 비해 시간이 매우 짧아 무시할 수 있을 정도이다.
CST와 CS의 커플링 효과로 Node P의 DATA 전압은 이 구간 동안 유지가 된다.

## Slide 6
SCAN(n)
SCAN(n+1)
DATA
Node P
Compensation period
1
2
3
IOLED
VDD
SCAN(n)
DATA
GND
M2
M1
Cst
Cs
M4
M3
Node P
GND
SCAN(n+1)
OLED
Scan(n+1) is applied and the voltage of Node P is bootstrapped through M4 to increase the voltage.
In this period, the current flows through the OLED through the VDD to emit light, but the time is very short compared to the frame time and can be ignored.
As the length of the CS increases, the capacitance increases, and as the voltage increases, enough compensation can be made for the Stretching of the M2.
Circuit Timing Scheme
Figure 1. Proposed Pixel Circuit Schematic
Figure 2. Timing Scheme
Notes: Scan(n+1)이 인가되면서 M4를 통해 Node P의 전압이 bootstrap이 되어 전압이 증가한다.
이 구간 또한, VDD를 통해 OLED에 전류가 흐르게 되어 발광하게 되지만 프레임 시간에 비해 시간이 매우 짧아 무시할 수 있을 정도이다.
CS의 길이가 증가할수록 정전용량이 커지게 되고, 그만큼 전압이 증가하여 M2에 Stretching된 충분한 보상을 할 수 있게 된다.

## Slide 7
SCAN(n)
SCAN(n+1)
DATA
Node P
Emission period
1
2
3
IOLED
VDD
SCAN(n)
DATA
GND
M2
M1
Cst
Cs
M4
M3
Node P
GND
SCAN(n+1)
OLED
As all the pulses go low level, the TFT in the circuit becomes M2 On, and the OLED emits light at this period.
It lasts until the next scan pulse, and it has the longest period of the three period.
Circuit Timing Scheme
Figure 1. Proposed Pixel Circuit Schematic
Figure 2. Timing Scheme
Notes: 모든 Pulse가 로우 레벨이 되면서 회로 내의 TFT는 M2만 on이 되고, 이 때 OLED가 발광하게 된다.
다음 Scan pulse가 들어오기 전까지 지속되며, 세 개의 구간 중 가장 긴 period를 가지고 있다.

## Slide 8
Simulation Parameter
1
Simulation Data
2
Simulation
Ⅱ

## Slide 9
The simulation was performed using the power values ​​shown in Table 1.
The simulation verified the current of the OLED over time and confirmed whether or not it compensates as the CS increases.
Simulation
Figure 1. Proposed Pixel Circuit Schematic
VDD
SCAN(n)
DATA
GND
M2
M1
Cst
Cs
M4
M3
Node P
GND
SCAN(n+1)
OLED
SCAN(n)
SCAN(n+1)
DATA
Node P
Figure 2. Timing Scheme
1
2
3
IOLED
Scan(n) | 0 ~ 10 V
Scan(n+1) | 0 ~ 10 V
Data | 2 ~ 4 V
VDD | 15 V
CS | 0.2pF
Table 1. V_Source and Capacitor Parameter
Simulation Parameter
Notes: 표 1에 있는 전원 값들을 이용하여 시뮬레이션을 진행하였다.
시뮬레이션은 시간에 따른 OLED의 전류를 확인하고, CS가 증가함에 따라 보상이 되는지에 대한 유무까지 확인하였다.

## Slide 10
Simulation
Chart: IOLED & ISTRETCHING
Chart: IOLED & ISTRETCHING
Figure 3. Data 2V, OLED currents and stretched OLED currents over time
Figure 4. Data 3V, OLED currents and stretched OLED currents over time
Chart: IOLED & ISTRETCHING
Figure 5. Data 4V, OLED currents and stretched OLED currents over time
Data is varied from 2 to 4 V and the results are simulated.
The value of CS at normal was 0.2 pF, and the value of CS was simulated at 0.24 pF assuming that it was 20% strained.
It can be seen in each figure that the current increases when it is stretching.
As the data increased, the growth rate decreased to 16.7%, 11.5%, and 7%, respectively.
Simulation Data
Notes: Data를 2~4 V까지 변화시켜, 시뮬레이션 한 결과이다.
Normal에서의 CS의 값은 0.2pF으로 하고, 20% Stretching 된 것을 가정하여 CS의 값은 0.24pF로 시뮬레이션하였다.
Stretching이 됐을 시에 전류가 증가하는 것을 각각의 그림에서 확인할 수 있다.
Data가 증가할 때마다 16.7%, 11.5%, 7%로 증가폭은 감소하는 경향을 보였다.

## Slide 11
Conclusion
We proposed a 4T2C pixel circuit which can be applied to a substrate which is subjected to stretching.
The proposed circuit is intended to be applied to a large area display.
The proposed circuit is distinguished from the rigid region and the stretching region and can be easily applied to a striped OLED display.
It was confirmed that the size change of CS(Stretching Capacitor) affects the change of IOLED.
As the data voltage increases, the increase of IOLED decreases, and we plan to revise and supplement it through simulation and experiments.
Notes: Stretching이 되는 기판에 적용할 수 있는 4T2C 구조의 화소 회로를 제안했다.
제안된 회로는 대면적 디스플레이에 적용하는 것을 목적으로 하였다.
제안된 회로는 Rigid 영역과 Stretching 영역을 구분하여, Stretchable OLED Display에 보다 쉽게 적용할 수 있다는 장점이 있다.
CS(Stretching Capacitor)의 크기 변화가 IOLED의 변화에 영향을 주는 것을 확인할 수 있었다.
Data 전압이 증가할수록 IOLED의 증가폭이 감소하는데, 앞으로도 추가적으로 시뮬레이션 및 실험을 통하여 수정 및 보완해 나갈 계획이다.

## Slide 12
Thank you for your attention