## Slide 1: AMOLED Pixel Circuit Composed of MOSFET
Hoseo University
Electronic Device Laboratory
Min Su Kang
Notes: Hello.
I’m Min Su Kang in Electronic Device Laboratory.
My Research theme is a AMOLED Pixel Circuit Composed of MOSFET.

## Slide 2: Outline
Introduction
AMOLED Pixel Circuit
  2T1C Pixel Circuit
  4T2C Pixel Circuit
Pixel Circuit Composed of MOSFET
  2T1C MOSFET Pixel Circuit
  4T2C MOSFET Pixel Circuit
Conclusion & Future works
Notes: First, I’ll talk about a AMOLED pixel circuit for stretchable display.
And then, i’ll show simulation results for two type of a pixel circuit.
Next, Let’s talk about a MOSFET pixel circuit and measurement results of a MOSFET pixel circuit.
At last, I’ll summarize presentation.

## Slide 3: Introduction
Source : Google image
Mobile Plastic
Display
Large Area
Rollable Transparent Display
All Size
Stretchable Display
Area Strain
Necessity of
Luminance Compensating Pixel Circuit
Figure 1. Generation of flexible display
Notes: Figure 1 shows a generation of flexible display.
In 3rd generation flexible display, so called Stretchable Display is defined as a display with an increased panel width.
In a stretchable display, panel area is changed by strain.
Area stretching reduces the luminance of the panel.
Therefore, a pixel circuit capable of compensating for luminance is required.

## Slide 4: 2T1C Pixel Circuit
A circuit composed of two TFTs, one capacitor
When the substrate is stretched,  the R, C of wiring increase  the characteristics of TFT changes
SW_TFT
DR_TFT
Data
Scan
VDD
Cst
VSS
OLED
TFT W/L | Sw_TFT | 10/10 [um]
 | Dr_TFT | 10/15 [um]
Capacitor | Cst | 0.05 [pF]
Figure 2. Conventional 2T1C pixel circuit
Table 1. Simulation parameter of 2T1C pixel circuit
Notes: Figure 2 shows conventional 2T1C pixel circuit.
It is composed of two TFTs and one capacitor.
When the substrate is stretched, R, C parameter of wire increase and the characteristics of TFT changes.

## Slide 5: 2T1C Pixel Circuit
Luminescence decreased due to area stretching
(a)
(b)
Figure 3. Simulation results of 2T1C pixel circuit (a) OLED current (b) Luminescence
그림의 글자가 너무 작습니다.
Notes: Figure 3 shows simulation results of area strain verse current and luminescence of OLED.
The OLED luminescence decreased due to area stretching.

## Slide 6: 4T2C Pixel Circuit
A circuit composed of four TFTs, two capacitor
Compensates for the change of luminance by area stretching
TFT W/L | T1 | 10/10 [um]
 | T2 | 10/40 [um]
 | T3 | 10/10 [um]
 | T4 | 10/10 [um]
Capacitor | Cst | 0.06 [pF]
 | Cs | 0.05 [pF]
Data
Scan[n]
VDD
Cst
VSS
OLED
Cs
Node P
Node Q
Scan[n+1]
T1
T2
T3
T4
Figure 4. Proposed 4T2C pixel circuit
Table 2. Simulation parameter of 4T2C pixel circuit
Notes: Figure 4 shows proposed 4T2C pixel circuit.
It is composed of four TFTs and two capacitors.
The stretching capacitor, Cs compensates for luminance when expanding the area.

## Slide 7: 4T2C Pixel Circuit
Scan[n] becomes high state, T1 and T3 are turned on and the voltage of Node P becomes Data voltage through T1.
At this time, other pulses remain low. The current flows through the OLED from VDD to the cathode.
The currents during this period can be neglected because the time of the current flows is very short t compared to the frame time.
A data voltage is stored at the node P is during this period.
SCAN[n]
SCAN[n+1]
DATA
Node P
1
2
3
IOLED
VDD
SCAN[n]
DATA
T2
T1
Cst
Cs
T4
T3
Node P
SCAN[n+1]
OLED
Node Q
Figure 5. Timing diagram of 4T2C pixel circuit (1)
Notes: Let’s explain the operation of the 4T2C pixel circuit with the timing diagram.
When Scan[n] becomes high state, T1 and T3 are turned on and the voltage of Node P becomes Data voltage through T1.
At this time, other pulses remain low. The current flows through the OLED from VDD to the cathode.
The currents during this period can be neglected because the time of the current flows is very short t compared to the frame time.
A data voltage is stored at the node P is during this period.

## Slide 8: 4T2C Pixel Circuit
When Scan [n] is low and Scan [n + 1] is high, the voltage of the node is bootstrapped by Cs through T4.
Although the OLED emits current through the VDD, the emission time is shorter than the frame time and can be ignored.
As the area increases, the capacitance increases, and the voltage stored in the Node P increases.  It is possible to compensate the luminance decreased by stretching.
SCAN[n]
SCAN[n+1]
DATA
Node P
1
2
3
IOLED
VDD
SCAN[n]
DATA
T2
T1
Cst
Cs
T4
T3
Node P
SCAN[n+1]
Node Q
OLED
Figure 6. Timing diagram of 4T2C pixel circuit (2)
Notes: When Scan [n] is low and Scan [n + 1] is high, the voltage of the node is bootstrapped by Cs through T4.
Although the OLED emits current through the VDD, the emission time is shorter than the frame time and can be ignored.
As the area increases, the capacitance increases, and the voltage stored in the Node P increases. It is possible to compensate the luminance decreased by stretching.

## Slide 9: 4T2C Pixel Circuit
All the pulses become low, and the TFT T2 becomes ON, and the OLED emits light.
It lasts until the next scan pulse, and it has the longest period among three segments.
SCAN[n]
SCAN[n+1]
DATA
Node P
1
2
3
IOLED
VDD
SCAN[n]
DATA
T2
T1
Cst
Cs
T4
T3
Node P
SCAN[n+1]
Node Q
OLED
Figure 7. Timing diagram of 4T2C pixel circuit (3)
Notes: All the pulses become low, and the TFT T2 becomes ON, and the OLED emits light.
It lasts until the next scan pulse, and it has the longest period among three segments.

## Slide 10: 4T2C Pixel Circuit
Luminance Compensation
Figure 8. Simulation results of 4T2C pixel circuit (a) OLED current (b) Luminescence
(a)
(b)
이동도와 문턱전압은 스트레칭에 의해 열화되고 밝기가 그렇지 않은 경우에 비해 더 어두워져야 맞는데… 이거 잘 못 됬습니다.
Notes: Figure 8 shows simulation results of area strain verse current and luminescence of OLED.
The OLED luminescence increased due to proposed circuit’s compensation effect.

## Slide 11: MOSFET Pixel Circuit
A typical AMOLED pixel circuit is composed of thin film transistors.
However, the TFT pixel circuit is small in size and currents are much low, which makes it difficult to measure the OLED current directly.
Therefore, the MOSFET pixel circuit was composed to verify the function of the pixel circuit.
The TFTs were replaced by a 2N7000 MOSFET.
Instead of the OLED, resistor was used in measure the current.
Notes: A typical AMOLED pixel circuit is composed of thin film transistors.
However, the TFT pixel circuit is small in size and currents are much low, which makes it difficult to measure the OLED current directly.
Therefore, the MOSFET pixel circuit was composed to verify the function of the pixel circuit.
The TFTs were replaced by a 2N7000 MOSFET.
Instead of the OLED, resistor was used in measure the current.

## Slide 12: 2T1C MOSFET Pixel Circuit
T1
Data
Scan
VDD
15 pF
VSS
1 MΩ
T2
Figure 9. (a) 2T1C MOSFET pixel circuit (b) Measurement result
(a)
(b)
Notes: Figure 9 shows 2T1C pixel circuit composed of MOSFET and measurement result.
For a voltage measurement, the OLED was replaced by a resistor.
The red line represents the scan voltage and the black line represents the data voltage.
The OLED voltages increased when the data voltage and the scan voltage are high.

## Slide 13: 4T2C MOSFET Pixel Circuit
Data
Scan[n]
VDD
15 pF
VSS
15 pF
Scan[n+1]
T1
T2
T3
T4
1 MΩ
(a)
(b)
Figure 10. (a) Cs=15 pF 4T2C MOSFET pixel circuit (b) Measurement result
Notes: Figure 10 shows proposed 4T2C pixel circuit composed of MOSFET and measurement result.
Same as 2T1C pixel circuit, the OLED was replaced by a resistor.
The red line represents the scan1 voltage, the blue line represents the scan2 voltage, and the black line represents the data voltage.
The OLED voltage increased proportional to stretching capacitor, Cs.

## Slide 14: Conclusions
The Cs increased due to area stretching.
As Cs increased, the OLED voltages increased due to the coupling effect.
Increased OLED voltage resulted in the increase of the currents and luminescence of OLED.
Therefore, the proposed 4T2C pixel circuit is suitable for a stretchable OLED display.
Notes: The Cs increased due to area stretching.
As Cs increased, the OLED voltages increased due to the coupling effect.
Increased OLED voltage resulted in the increase of the currents and luminescence of OLED.
Therefore, the proposed 4T2C pixel circuit is suitable for a stretchable OLED display

## Slide 15: Thank you for your attention.